Use of membrane PARODONCOL

in different bone grafting operations

(Instruction for use)

Preparations

Plates of the sizes 30x25х0.6 mm, of the weight approximately 0.25 g, of white colour. Contains an active surface (with a thickening of white colour). Manufacturing of other sizes and forms is possible.

Property

PARODONCOL by preventing germination of the epithelial cells into the bone defect intensifies the bone formation (osteogenesis) and stimulates a wound-healing in osseous and periodontal tissues and is completely resorbable

Treatment

The material is used in various reconstructive operations in maxillofacial region: closure of cleft palate, cleft alveolar process, restoration of cortical plate, alveolar process correction, etc. It is indicated for dental implantation

Uses

The parameters of incision is a determining factor for conservation of soft tissues and for ensuring maximal blood supply. A flap should have the wide basis.

When operating surgeon separates mucoperiosteal flap and bone surface in order to prepare the surface of the bone tissue.

After careful curettage, removal of epithelium from the flap and the therapy one fill in the osseous cavity (pocket) in case of significant depth with Hydroxyapol or Kolapol КP-3. In bone grafting operations the bone is freshened up by a bore or cutter. PARODONCOL is put with an active surface on a bone surface with overlap of 2-4 mm of osseous defect by membrane. If necessary the fragments of any configuration can be easily cut from the material. One should fix PARODONCOL on osseous tissue by any of the accessible ways to prevent the slipping down.

For elasticity moisten the material with the patient blood, physiological solution or any antibiotic solution, or furacillin, etc.

After the material implantation mucosa is sewed up for 6-8 days. One should not forget that inside tissues the material is swelling a bit, that’s why attention should be paid to that the sutures are not strained by the excess of the implanted material. In case of considerable oedema on 2nd-3rd day after the operation surgeon let the exudation through the sutures. The thorough cutting out of the material allows to get the appropriate form to prevent the excessive strain of a flap and a suture will quicken the healing of soft tissues.

Prescribe to the patient antihistamine drugs, if necessary – analgesics and antibiotics. Antibiotics, immunomodulators and other medicines can be applied with PARODONCOL by impregnation before use.

Pay special attention to the oral hygiene.

Proprietary preparations

The product is available in sterile packing. Do not sterilize additionally

Contraindications

Active inflammatory process (found during the operation).